## Slide 1: Robust fetal ecg detection from abdominal recordings
Implementation of Martens et al. (2007) and evaluation on PhysioNet Challenge 2013 Set-A
Sofia Maggioni | matr. 75788A
Biomedical Signal Processing | Università degli studi di Milano

## Slide 2: Context and clinical challenge
Core idea: progressively clean the abdominal ECG, remove the maternal ECG, then detect fetal QRS complexes.
Dataset used: PhysioNet Challenge 2013, Set-A
Main record: a14.
Batch evaluation: a10, a12, a13, a14, a15
.dat = signal | .hea = header | .fqrs = fetal reference beats
«To non-invasively detect and extract the weak fetal electrocardiogram (fECG), which is completely masked in abdominal recordings by the dominant maternal ECG (mECG) and severe biological and instrumental noise.»

## Slide 3: Roadmap – pipeline overview
A multi-stage, modular workflow for maternal ECG suppression, fetal detection, and morphological reconstruction
S1
Data ingestion
S2
Baseline removed
S3
Power-line removed
S4
upsampling
S5
Mathernal ECG removed
S6
Fetal ECG reveal
Preprocessing: remove baseline wander and attenuates to 50 Hz the power-line interference.
Phase S2 & S3
Upsampling: increases the sampling rate from 100Hz to 200Hz, halving the sampling interval to 0.5 ms.
Phase S4
Post processing & validation

## Slide 4: Baseline wander removed
From S1 to S2
Baseline wander: is a low-frequency disturbance (<1Hz) superimposed on the ECG signal. This prevents the waveform from returning to the isoelectric line (zero) between successive beats, causing the R-peaks to start from shifting baselines and introducing detection errors.
A high-pass FIR filter removes very slow components while preserving the QRS peaks.
For this filter I decide to apply a cutoff of 3Hz

## Slide 5: Power-line interference
From S2 to S3
Power-line interference: is a narrow-band noise occurring at 50 Hz and its higher harmonics (100 Hz and 150 Hz).
I use a time-adaptive estimation and subtraction method
1° I Estimate harmonic amplitude and phase Synthesize estimated sinusoids Subtract from signal.
2° I perform a quantification of the removed interference (RMS).
3° identify the channel with the highest disturbance, and compare the results

## Slide 6: upsampling
From S3 to S4
Upsampling: Increases the sampling frequency from 1000 Hz to 2000 Hz to enable fine alignment of the average template with each R-peak.
The sampling interval is reduced from 1 ms to 0.5 ms,
doubling the number of samples per channel from 60,000 to 120,000.

## Slide 7: Mqrs detection
S4
To detect mathernal QRS I use three different steps:
1° PCA (principal component analysis)
2° I reconstruct the ideal maternal QRS complex
3° I find the actual beats thanks to an index table that I am going to use on the next step.

## Slide 8: Mqrs removed
From S4 to S5
For each maternal beat, the algorithm uses the 10 preceding maternal beats to build a local maternal ECG estimate. The estimate is split into P-wave, QRS-complex, and T-wave zones. Each zone is scaled separately, then the full estimated maternal ECG is subtracted.
After that As a simple check, I compare the RMS amplitude around the maternal QRS positions before and after cancellation. A lower RMS after cancellation means that the large maternal QRS peaks were reduced.

## Slide 9: fqrs removed
From S5 to S6
I detects fetal QRS positions and evaluates them against the reference annotations supplied by PhysioNet.
I use .fqrs file, converting it into 2000 Hz.
A detected fetal beat is counted as correct if it falls within 50 ms of a reference fetal beat. This gives true positives, false positives, false negatives, sensitivity, positive predictive value, and F1-score. I also calculate the mean fetal R-R interval and the estimated fetal heart rate from the detected fetal beats.

## Slide 10: Batch evolution on other records
For the project, it is useful to show that the implementation can also be tested on multiple recordings
We use five Set-A records: a10, a12, a13, a14, a15
These four records check whether the same code also runs on different signals. `a11` was not used in this small final batch because the PCA step did not converge on that record with the fixed parameters